Face recognition & Temperature terminal

( 8inch )

Application:

Suitable for office areas, hotels, passage gates, office buildings, schools, shopping malls,shops, communities, construction sites and other public services and management projects where face access control is required.

Product features:

- Wide dynamic monocular living anti-counterfeiting, completely solving the deception of various photos on various uploads;

2. Support LED intelligent fill light;

3. Support serial port, Wiegand 26-bit, 34-bit output, and support output content configuration;

4. Real-time body temperature monitoring, and body temperature range is accurate to 0.3 degree, body temperature detection distance is 0.3-0.5 meters;

5. Support the device to store thousands of people locally

6. The LAN device supports simultaneous storage of 20,000 face photos and 1 million recognition records.

7. 1: N face recognition, the face database supports 20,000 faces,

8. The accuracy ratio of 1: 1 personal identification is over 99%;

9. Face tracking and detection takes about 20ms;

10. Feature identification takes 0.5ms

11. Support stranger detection, stranger level can be configured;

12. Support live photo saving on face recognition or stranger detection;

13. Support HTTP port connection;

14. Support public network and local area network management

15. Support screen display of content configuration

16. Support identifying distance configuration

Parameters:

| operating system | Android 7.1 and above |
| --- | --- |
| processor | CPU 4 core RK3299 |
| display | 8-inch, full-view IPS LCD screen |
| Display resolution | 800*1280,lightness 400cd |
| Fill light | Infrared, LED Fill light |
| Camera | 200W |
| Working environment | Indoor and semi-outdoor without sunlight |
| Operating temperature | -10℃～60℃ |
| Power supply | DC12V |
| Face recognition algorithm | Despise |
| Face Detection | Support simultaneous detection and tracking of 5 people |
| Recognition speed | ≤200ms |
| Temperature measurement accuracy Fever alarm | ±0.3℃ When the detected human body temperature exceeds 37.2 ℃ (adjustable), an alarm is issued |
| Face library | 20,000 Local Face Library |
| Personnel management | Add, delete, and modify personnel on local applications |
| Recognition mode | Face recognition, temperature detection |
| Settings management | Equipment management, rights management, personnel / photo management, record query, etc. |
| Network module | Support wired, 2.4Gwifi, 4G network card |
| card module (Optional) | Support IC / ID card reader |

Product Specification

| Product model | Category | Performance |
| --- | --- | --- |
| camera | Resolution | 200W |
|  | Types | RGB + IR |
|  | Aperture | 4.0mm |
|  | Focus | 0 to 2 meters |
|  | White balance | Auto |
| Screen | size | 8-inch, full-view IPS LCD screen |
|  | Resolution | 1280 * 800, brightness 400cd |
| Processor | CPU | 4 cores，RK3288 |
| RAM | DDR3 | 2GB |
| ISP | Image Processing | Built-in dual-channel ISP |
| Local storage | Tf card | 8GB |
| Accessories | Fill light | Infrared, LED lights |
|  | Card reader module (Reserved) | IC / ID card reader, ID card reader and thermal imaging temperature detection module |
|  | Network module | Support wired, 2.4Gwifi, 4G network card |
| Port | Audio | 1 Audio line out |
|  | USB port | USB2.0 and 2micros |
|  | Serial port 232 | 2 RS232 ports, 1 WG input, and with WG output |
|  | Wiegand port | 2.5mmX2PIN |
|  | Reset port | Lateral pore position, external buttons |
|  | OTG port | In Channel 1 |
| Functions | Offline locally use | 20 thousand local face database |
|  | Face Detection | 20 thousand local face database |
|  | 1: N face recognition | Support one in 10,000 error recognition with 99% pass rate |
|  | 1:1 | Support optional card swiping module, ID card module which can realize 1: 1 face identification |
|  | Stranger detection | Support |
|  | Distance recognition adjustment | Support |
|  | Remote upgrade | Support |
|  | Device port | Including equipment management, access control, personnel or photo management, record query, etc. |
| General parameters | Protection level | For semi-outdoor or pure outdoor use |
|  | Power | DC12V |
|  | Operating temperature | -10℃-60℃ |
|  | Working humidity | 10%-90% |
|  | Static electricity | 4K/8K |
|  | Battery radiation | Not exceeded |
|  | Power consumption | 5W MAX |
|  | Equipment weight | 1.6KG |
|  | Equipment size | 374*135*85mm |