## 1.Access controller

## 2.Barcode Reader

The fixed barcode scanner can read bar code information on mobile phone screens and paper documents, mainly used in electronic voucher, mobile marketing, office automation and other fields.

Features of the fixed barcode scanner:

LCD reading ability: It can recognize the main 2D barcode and various 1D barcodes displayed on the screen of the mobile phone.

Paper code reading ability: The main 2D barcode printed on paper and various 1D barcodes can also be read.

High-speed reading: For different mobile phone LCD screens, generally have different contrast, color and reflection level, the scanner can be quickly read.

Read parameters:

Microprocessor: IOTC 0370 CHIP

 Reading method: 752*480 CMOS

 Interface: RS-232 (9.6~115.2Kbps) / USB 1.1 (HID-KBW, HID-POS)

Read the reading system: 2D, PDF417, Data Matrix, QR Code

1D EAN-13 (with additional code), EAN-8 (with additional code), UPC-A (with additional code), UPC-E (with additional code), ISSN, ISBN, Codabar, Code 128 (including FNC1, FNC2, FNC3 subsets), Code 93, ITF-6, ITF-14, Interleaved 2 of 5, Industrial 2 of 5, Standard 2 of 5, Matrix 2 of 5, GS1 Databar (RSS-Expand, RSS -Limited, RSS-14), Code 39 (including Code 39 FULL ASCII), Code 11, MSI-Plessey, Plessey

 reading mode: induction reading

 reading accuracy: 10mil

Light source :White LED

 reading code window: 38.3mm × 60.4mm

Print contrast: ≥30%

Field angle: Diagonal: 85°, Horizontal: 63.7°, Vertical: 70°

Maximum power consumption: 1.75W

Indication: Buzzer

 size (length x width x height): 78.2 × 67.2 × 62mm

 Weight: 300g

Environment



Data line: RS-232 data line, RS-232 Working temperature: -10 ° C - +50 ° C

 Storage temperature: -20 ° C - +60 ° C

 Humidity: 5% - 95% (no condensation)

 Ambient light: 0 ~ 100,000 LUX

International Certification: FCC Part15 Class B, CE EMC Class B

Accessories list

data line, used to connect the information receiving host with adapter interface.

USB data cable, USB data cable, used to connect to the information receiving host.

 Power Adapter: 5V power adapter, with the data cable to power the scanner.

The output is: DC5V, 0.5A; Input is: AC100~240V, 50~60Hz

# Text boxes

Description:

Using Data Flash and ferro electric memory, power-down data is not lost, the controller card capacity of 20,000, the event capacity of 100,000

The control panel has a DIP switch, you can set the DIP switch settings to enable different functions; speech function;

The size of the control panel is 10 * 30cm, can be installed in the space is relatively small inside the gates;

Channel access control controller technical parameters

1, power supply

Supply voltage: 12V DC

Location: J15 12V (then power is positive), GND (then power negative)

2, communication

Location: J18

RJ45 10M / 100M network communication

Default IP address: 192.168.1.15

3, restart

The door panel is powered off and then powered on as a reboot.

4, Wiegand input interface 2 way

1st way:

Position J1: 1D1, 1D0, 12V, GND

Technical parameters:

The legal signal output, control J10 relay LOCK1

Illegal signal output, control J11 relay LOCK3

5. External input 6 way

Channel access control controller technical parameters

1, power supply

Supply voltage: 12V DC

Location: J15 12V (then power is positive), GND (then power negative)

2, communication

Location: J18

RJ45 10M / 100M network communication

Default IP address: 192.168.1.15

3, restart

The door panel is powered off and then powered on as a reboot.

4, Wiegand input interface 2 way

1st way:

Position J1: 1D1, 1D0, 12V, GND

Technical parameters:

The legal signal output, control J10 relay LOCK1

Illegal signal output, control J11 relay LOCK3

5. External input 6 way

Divided into two groups, each group 3, under normal circumstances, the first group can be connected to three pairs of infrared, the second group of spare

position:

J5: BTN1, SEN1, N1, GND

J6: BTN2, SEN2, N2, GND

2nd way:

Position J2: 2D1, 2D0, 12V, GND

Technical parameters:

The legal signal output, control J10 relay LOCK2

Illegal signal output, control J11 relay LOCK4