TQJ-D0638XDZ-M

Application

Used in 2G/3G/4G/5G/WLAN system

| Electrical specifications |
| --- |
| Frequency range (MHz) | 617～960 | 1710～2700 | 3300～3800 |
| Polarization | 2*Linear |
| Maximum Gain (dBi) | 4 | 5 | 6 |
| Horizontal beam width (°) | 360 |
| Vertical beam width (°)（Typical values） | 80 | 50 | 40 |
| Isolation (dB) | ≥16 | ≥20 | ≥25 |
| Impedance (Ω) | 50 |
| VSWR | ≤2.0 | ≤1.8 |
| Intermodulation IM3 (2×43dBm carrier) | ≤-150 dBc |
| Maximum power (W) | 50 |
| Lighting protection | DC Ground |
| Mechanical specifications |
| Connector | 2*4.3-10 Female |
| Connector position | Bottom |
| Exposed cable size (cm) | 30(or customer requirement) |
| Height/width/depth (mm) | Φ207*56 |
| Packing size (mm) | 213*168*204 |
| Weight (kg) | 0.6 |
| Radome material | ABS |
| Radome color | White |
| Operating temperature (℃) | -40～60 |
| Application | Indoor |
| Mounting | Nut |
| 617～960MHz Typical pattern: | 1710～2700MHz Typical pattern: | 3300～3800MHz Typical pattern: |

# Text boxes

Product pictures

Product size

Installation Sketch

- Drill a round hole Φ25mm～Φ30mm on the ceiling.

2、Match the antenna to the round hole.

3、Fix the antenna onto the ceiling with the screws.

Attention!

The hole on the ceiling must be slightly bigger than the antenna connector flange, and the antenna base plate should be in close contact with the ceiling, which influences the performance of the antenna.