Product introduction and use
This machine is an automatic CNC machining machine for machining the inner and outer cylindrical surfaces of the parts, conical surface, end surface, grooving and chamfering. It is especially suitable for brake hubs, drums, clutch pressure plates and flywheels. Processing of parts such as shells.

PARAMETER

| ITEM | Parameter |
| --- | --- |
| Max swing diameter | 1250 MM |
| Max. Length of Workpiece | 1000 MM |
| Max processing height | 1600 MM |
| Max loading weight | 5000 KG |

| Specifications | VTC1250 |
| --- | --- |
| Max. turning diameter of workpiece | 1250mm |
| Max.turning diameter | 1000/1250(disc type) |
| Vertical travel of tool post | 1000mm |
| Horizontal travel of tool post | -50-700mm |
| Spindle model | A2-11 |
| Spindle load | 1500KG |
| Spindle speed range | 50-600rpm,1:2.5 Speed ratio |
| Main motor power | 30kw(Rated speed750) |
| X axis rapid feed traverse | 15m/min |
| Z axis rapid feed traverse | 12m/min |
| Cutting feed speed | 0.1-5000mm/min |
| X axs motor power/Torque | 3.14 kW /20NM |
| Z axs motor power/Torque | 3.14 kW /20NM brake |
| Tool post type | 4 station electric tool post |
| Tool shank size | 40×40mm |
| Chuck diameter | 1000mm（manual 4 jaw） |
| Positioning accuracy | ±0.01mm |
| Repeat positioning accuracy | ±0.005mm |
| Machine weight | ≈12800kg |
| Overall dimensions | 3060×3010×3500mm |