Dayang Medical

Name of Parts

1. Hand Grip                  2. Backrest               3. Armrest pad

4. Height Adjustable armrest      5. Chest fixing            6. Brake Lever

7. Rear Wheel                 8. Legrest                9. Fork

10. Front Castor               11. Pillow (Head rest)       12. Cross Tube

13. Foot Plate                 14. United Brake           15. Recline Brake

Part I: How to Assemble

- Wheelchair frame

- Take out wheelchair frame from box

- Push down the cross-bar by hands

- Make sure the frame is fully unfolded

Step 1                Step 2             Step 3

Caution: Do not put your hands under the tube to avoid hands be nipped

- Seat board

- Fix the four plastic clamps on seat tube

- Lock it by the two screws under seat

Step 1                                   Step 2

- Backrest board

- Fix the four plastic clamps on backrest tube

- Lock it by the two screws at back side of backrest

- Headrest (pillow)

- Insert the supporting bar on the two backrest tubes

- Put the pillow tube into the supporting bar and fix by screw

Step 1                                        Step 2

- Armrest

- Fix the holder of armrest into seat frame, and choose the right position then fix by screw

- Insert armrest tube, and choose the suitable height position then fix it by screw

Step 1                                     Step 2

- Leg rest

- Fix leg rest on the two bolts of wheelchair frame

- Put the leg rest turn to direction of center of seat

Step 1                                    Step 2

- Anti-tipper (fix it by locking the bolt)

- Leg rest fixer

Fix it by screws under the seat

Part II: Functions

- Backrest adjustment

1). Stand behind of wheelchair and put left hand on the adjusting lever

2). Lift up the lever to adjust backrest position then release the lever

- Seat adjustment

1). Stand behind of wheelchair and put right hand on the adjusting lever

2). Lift up the lever to adjust seat position then release the lever

- Brake

1). Pull the brake handle for locking

2). Push the brake handle for unlocking

- Auto-locking Brake (for nursing use)

1). Pull the brake handle lever for locking

2). Pull the button for releasing brake

Step 1                                   Step 2

- Leg rest

1). Footplate and leg support pad can be foldable (picture 1)

2). Pull the button to take out leg rest (picture 2)

3). Leg support pad height adjustable by loosening screw (picture 3)

4). Elevating: lift up leg rest to the suitable position (picture 4)

5). Push adjusting lever to low down leg rest position (picture 5)

Picture 1                 Picture 2                Picture 3

Picture 4                                        Picture 5

- Pillow

Push left and right sides of pillow by hands to suitable position (picture 2)

Picture 1           Picture 2                Picture 3

# Text boxes

14

15

5

4

6

7

8

9

10

13

12

3

2

11

1