Wheelchair DY1868LJ

| DY1908LAJQ | 64 | 29 | 46 | 60 | 15 | 48 | 93 | 104 | 40 | 43 | 100 | 80*28*74 1PC/CTN | 14.5/16.5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

USER’S  MANUAL

1. Hand Grip            2. Backrest             3. Armrest pad

4. Flip-Up armrest     5. Hand rim            6. Brake Lever

7. Rear Wheel           8. Legrest              9. Fork

10. Front Castor         11. Side Panel           12. Cross Tube

13. Foot Plate           14. Auto-lock United Brake

How to Lock and Unlock the Wheelchair

It is very important to lock the Wheelchair when simply sitting on it.

A. This is how the brake looks like when the wheelchair is unlocked.

B. Hold the brake lever and move it forwarder, as the arrow indicates.

C. When you hear a “Snap”, the wheelchair is locked.

D. This is how the brake looks like when the wheelchair is locked.

To unlock the wheelchair is operate the other way around.

How to Use United Brake

- This is how the brake looks when it is release;

- Lift the long bar until you hear a “snap”, in this case, the brake is locked;

- This is how the brake looks when it is locked;

- Lift the short bar until you hear a “snap”, in this case, the brake is released.

How to fold the Wheelchair

- Take out the head rest and footrest before you fold the wheelchair.

- Pull up the string on both sides of the seat frame, and the wheelchair will fold as you pull.

# Text boxes

14

4

5

6

7

8

9

10

13

12

11

3

1

2

String