Wheelchair DY1953LQ

| DY1953LQ | 53 | 30 | 46 | 60 | 20 | 53 | 103 | 103 | 45 | 39 | 100 | 80*32*89 1PC/CTN | 17/19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

USER’S  MANUAL

1. Hand Grip            2. Backrest             3. Armrest pad

4. Flip-Up armrest     5. Hand rim            6. Brake Lever

7. Rear Wheel           8. Legrest              9. Fork

10. Front Castor         11. Side Panel           12. Cross Tube

13. Foot Plate

How to Assemble and Detach the Wheelchair

1). Armrest

A. Pull the flip back Button.  B. Press down or lift up the armrest.  C. Done.

2). Legrest (From Left to Right)

A. Lift up the foot plate;

B: Pull the Swing Pin to the opposite side;

C. Turn the legrest as the blue arrow indicates;

D. Lift Up the Legrest.

E. Done.

How to Lock and Unlock the Wheelchair

It is very important to lock the Wheelchair when simply sitting on it.

A. This is how the brake looks like when the wheelchair is unlocked.

B. Hold the brake lever and move it forwarder, as the arrow indicates.

C. When you hear a “Snap”, the wheelchair is locked.

D. This is how the brake looks like when the wheelchair is locked.

To unlock the wheelchair is operate the other way around.

How to Quick Release the Rear Wheel

A. Press the quick release button with one hand and hold the armrest with the other.

B. Keep pressing the button and pull the rear wheel out as the arrow indicates.

C. Take out the rear wheel.

D. When in narrow places, you could take out the rear wheel. There are two anti tilting castors at the back of the wheelchair. In this case, the normal wheelchair can turn into a transit wheelchair temporarily.

How to fold the Wheelchair

- Take out the head rest and footrest before you fold the wheelchair.

- Pull up the string on both sides of the seat frame, and the wheelchair will fold as you pull.

# Text boxes

4

5

6

7

8

9

13

12

3

11

10

2

1

Swing Pin

String