1 Port 698-2690MHz Indoor Omni Antenna

Applications:

- 698-2690MHz

- Omni antenna

Features:

- Wide band

Connector:

- N-Female

| Electrical specifications |
| --- |
| Frequency range (MHz) | 698-960 | 1710-2690 |
| Polarization | Vertical | Vertical |
| Gain(dBi) | 2 | 6 |
| Horizontal beam-width(°) | 360 | 360 |
| 3dB Vertical beam-width(°) | 65 | 45 |
| VSWR | ≤1.8 |
| Intermodulation IM3(dBc) | ≤-150dBc(@2*43dBm) |
| Impedance(Ω) | 50 |
| Maximum input power(W) | 50 |
| Lightning protection | DC grounded |

| Mechanical specifications |
| --- |
| Connector | 1×N-Female |
| Connector position | Bottom |
| Size(mm) | Φ 186x 85 |
| Gross weight(kg) | 0.42 |
| Wind resistance(km/h) | 210 |
| Reflector material | Aluminium |
| Radome material | ABS |
| Radome color | Gray |
| Operating temperature(℃) | -40～65 |
| Waterproof | IP65 |

2690MHz