- T501 document scanner

| Model： | T501 |
| --- | --- |
| Appearance： | Folding upright, plastic shell + metal aluminum parts |
| Base Size： | 440*395mm |
| Scanner： | Unstretched: 308*126*126mm, stretched: 308*126*340mm |
| Net/Gross Weight: | 1.04KG/0.8KG |
| Product Lens： | 16MP |
| Shooting Range： | A4 and below documents, business cards, ID cards, etc., can be cropped and shot |
| Lens Structure: | Vertical 180 degrees (stretchable, not adjustable) |
| Resolution: | 4260×3140 dpi |
| OCR： | （OCR）&Wold /Excel /Pdf /TXT /CSV |
| Mirophone： | no |
| Image Format: | BMP /Jpeg /Gif /Png /Tif/PDF |
| Video Format: | Avi |
| Shooting Lens: | auto focus |
| Sensor： | CMOS |
| Color Digits: | 24 bits |
| Image Adjustment： | Brightness adjustment, exposure adjustment, saturation adjustment, sharpness adjustment, color selection, gain control, etc. |
| Product Features: | Remake archiving, e-book control, signature making (stamp tool), positive and negative merging, barcode recognition, two-dimensional code recognition, OCR text recognition, automatic correction, DV image recording, whiteboard display function, video function, etc. |
| Exposure/White Balance: | automatic |
| Light Source： | adjustable brightness |
| Model： | Natural light + LED light fill light |
| Appearance： | blue power light |
| Interface: | USB2.0 requires no external power supply |
| Operating Voltage: | 4.75V - 5.25V |
| Battery Type：： | USB5V power supply |
| Working Current: | 490mA |
| Surroundings： | -30°C to +80°C (storage temperature) / -20°C to +50°C (operating temperature) |
| Application System： | Applicable to WindowsXP SP2/SP3, Windows Vista, Windows7 operating system and above (minimum configuration requirements: P4/equal CPU, 512M memory, 80G hard disk; higher recommended) |