33 10-40KVA SPECS

| MODEL | 33 10KS PLUS | 33 10KVA PLUS | 33 20KS PLUS | 33 20KVA PLUS | 33 30KS PLUS | 33 40KS PLUS |
| --- | --- | --- | --- | --- | --- | --- |
| Rated power | 10KVA/8KW | 20KVA/16KW | 30KVA/24KW | 40KVA/32KW |
| Input | Range of voltage（full load） | 207~475Vac 3P4W+G |
|  | Range of frequency | 40-70Hz(adjusted) |
|  | Power factor | ≥0.99 |
| output | Rated voltage | 380Vac(1±1%) 3P4W+G |
|  | frequency | 1.The output frequency synchronizes with the input frequency when the input frequency is in the range of 46 Hz~ 54 Hz. 2.The output frequency is 50Hz when the input frequency is not in the range of 40 Hz~ 46 Hz and 54Hz~60Hz. 3.BAT mode:50Hz. |
|  | Rated current | 15A | 30A | 45A | 61A |
|  | Power factor | 0.8 |
|  | Distortion | ≤3% |
|  | Ratio | 3：1 |
|  | Over load | 105% ±5% < Load ≤ 125% ± 5% 60s transfer to bypass 125% ±5% < Load < 150% ± 5% 30s transfer to bypass Load > 150% ± 5%, 300ms transfer to bypass |
| Line—bat transfer time | 0ms |
| Efficiency | > 90% | > 91% |
| Bat | Rated voltage | 192Vdc | 192Vdc×2 |
|  | No. | 16 | 32 |
|  | Charging current | 7.5A | 1A | 7.5A | 1A | 5.5A |
| Size (L*W*H)mm | 533*260*501 | 560*260*717 | 710*260*717 | 710*260*717 |
| Weight | 26kg | 72kg | 57.5kg | 98kg | 58.5kg | 62kg |
| Work temp.(℃) | 0℃～40℃ |
| Work humidity | 20%～95％ |
| Noise（dB） | ≤60dB |