3XXX Pol Tube Antenna 3×698-960/6×1710-2690MHz 65°/65° 14/17.5dBi 0°-10°/0°-10° Replaceable RET

Electrical Specifications

| Frequency Range (MHz): | 3×698-960(R1) | 6×1710-2690 (Y1,Y2) |
| --- | --- | --- |
|  | 698-803 | 790-862 | 824-894 | 880-960 | 1710 -1990 | 1920 -2200 | 2200 -2490 | 2490 -2690 |
| Gain (dBi), | 13.0±0.5 | 13.3±0.5 | 13.6±0.5 | 14.0±0.5 | 16.0±0.5 | 16.2±0.5 | 17.0±0.5 | 17.2±0.5 |
| Return Loss (dB): | >14 (VSWR<1.5) |
| Polarization: | ±45° |
| Horizontal 3dB Beamwidth (°): | 73 | 69 | 68 | 71 | 68 | 63 | 60 | 58 |
| Vertical 3dB Beamwidth (°), | 17.0 | 15.5 | 14.7 | 13.5 | 7.5 | 6.8 | 6.0 | 5.5 |
| Electrical Downtilt (°): | 0-10 | 0-10 |
| RET Type: | RET Cascade SRET, AISG 2.0, Upgradeable |
| 1st Upper Sidelobe Suppression (dB): | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 |
| Front to Back Ratio 180±300(dB): | 23 | 24 | 25 | 25 | 25 | 25 | 25 | 25 |
| Cross Polar Ratio 0° (dB) | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 |
| Intraband Isolation (dB): | 26 | 26 |
| Interband Isolation (dB): | 28 |
| Max. Power Per Port (W): | 250 | 200 |
| Intermodulation IM3 (dBc): | <-150 (2×43 dBm) |
| Impedance (ohm): | 50 |
| Lightning Protection: | DC Grounded |
| Connector Type: | 18×4.3-10 Female |

Mechanical Data

| Antenna Dimensions (mm): | Φ450(Diameter)×1360(Length, mounting base excluded ) |
| --- | --- |
| Packing Dimensions (mm): | 1810(Length)×580(Width)×700(Height) |
| Antenna Net Weight (kg): | 84 |
| Antenna Gross Weight (kg): | 125 |
| Radome Material: | Fiberglass |
| Mounting Kits (Included): | Flange Mounted |

Environmental Ratings

| Humidity: | 95%RH@+30℃ |
| --- | --- |
| Temperature (℃): | -40～+70 |
| Wind Load @150 km/h (N): | 573 |
| Max.Wind velocity(km/h): | 200 |

Internal RET Specifications

| RET Type: | Replaceable RET |
| --- | --- |
| RET protocol: | AISG 2.0 /3 GPP |
| Input voltage range(V): | 10-30 DC |
| Power consumption(W): | < 5 (motor activated , single RET) < 1 (stand by, single RET), < 1.5 (stand by, 12V) |
| Adjustment time (full range) (s): | < 120 (typically, depending on antenna type) |
| RET connector: | 1 pair of AISG 5 pin male & female per sector |
| Pin assignment according AISG: | 8 pin circular connector conforming to IEC 60130-9 - Ed. 3.0 |
| Lightning protection (kA): | 5 (8/20 μs Differential mode), 8 (8/20 μs Common mode) |

Typical Patterns

| Azimuth(Low band) | Elevation(Low band) | Azimuth(High band) | Elevation(High band) |
| --- | --- | --- | --- |