One-to-tow automatic mask production line

※ The three layers of fabric on the top layer, the bottom layer, and the bottom layer are automatically aligned and fed. The bilaterally symmetric ultrasonic continuous blanking is cut off by continuous roller blanking, and then diverted to two stations for earband welding to improve production efficiency. The stacking code is automatically counted after it is taken.

※  The production adopts one-to-two structure, one mask body passes through the transmission system, Automatic delivery and shunting to two sets of earband automatic welding stations.

※ It can realize automatic feeding shear and ultrasonic welding of nose    ※ High-speed production, about 100,000 masks per day (24h).

※ Produce a variety of different products, and follow the change of abrasive tools to produce products of different shapes and specifications

| One-to-tow automatic mask production line system |
| --- |
| Mask type | Disposable earband flat mask |
| Design capacity | about 60-80 piece / min |
| Applicable material | PP non-woven composite fiber |
| Applicable layer | 3/4 layer |
| Processing method | Ultrasonic welding |
| Control method | touch screen automatic control |
| Air pressure | 0.5 0.7MPa (flow rate: 300L / min) |
| Power | 14KW |
| Working voltage | AC220v/50Hz |
| Footprint | 6500mmx3500mmx1500mm |
| Quality （KG） | 1500 |