## Slide 1
MODEL: LC-LED-AAA-300S
Lecheng Intelligent LED Solar Simulator
The Ideal Choice for Perovskite Photovoltaic Testing
Lecheng Intelligent

## Slide 2
Core Technical Advantages Optical Shaping System for More Accurate Testing
Competitor Limitations
• Lack of optical shaping, direct LED emission
• 30-40° light divergence, non-parallel light
• Short working distance, small/non-uniform area
Lecheng Intelligent's Breakthrough
• Complete optical shaping: Lens + Integrator
• Collimation angle < 5°, true parallel sunlight
• 50cm working distance, 300mm uniform spot
Indicator
Competitor
Lecheng (LC-LED-AAA-300S)
Collimation
30-40° (Divergent)
< 5° (Collimated)
Working Dist.
Short
50 cm
Area
Small/Non-uniform
300 × 300 mm (Class A)
* Diagram text in Chinese; see left for English details

## Slide 3
International A+ Standard Certification Performance Exceeding Industry Requirements
The product has been rigorously tested by third-party authoritative institutions, with all core indicators meeting or exceeding the highest requirements of IEC 60904-9 Edition 3 international standards.
Spectral Match
A+
•
Coverage: 350nm - 1200nm full spectrum.
•
All six key wavelength bands achieve A+ standard.
•
Ensures accurate spectral response testing for perovskite materials.
Irradiance Uniformity
A
•
Effective irradiation area: 300 × 300 mm.
•
Non-uniformity ≤ 2%.
•
Ensures consistency in large-area device testing.
Temporal Stability
A+
•
Short-term stability ≤ 0.25%.
•
Long-term stability ≤ 1%.
•
Supports transient pulse (>200ms) and steady-state continuous (24-1000h) testing.
Test Standard: IEC-60904-9-2020
Report Number: alsolute-2025X
Overall Rating:A+

## Slide 4
Precise Spectral Reproduction Designed Specifically for Perovskite Photovoltaics
LC-LED-AAA-300S covers a broad spectral range from 350nm to 1200nm, perfectly matching the full-band absorption characteristics of perovskite solar cells from ultraviolet to near-infrared.
Wavelength Band (nm)
Measured Ratio
Grade
300 - 470 (UV-Blue)
1.0030
A+
470 - 561 (Blue-Green)
1.0241
A+
561 - 657 (Green-Yellow)
1.0311
A+
657 - 772 (Red)
1.0375
A+
772 - 919 (Near-IR)
0.9783
A+
919 - 1200 (Near-IR)
0.9261
A+
Measured Spectral Chart: Highly consistent across all bands

## Slide 5
Flexible Testing Capabilities Meeting Multi-Scenario R&D Requirements
Wide-Range Irradiance
0.3 ~ 1.2 sun
300 - 1200 W/m² Continuously Adjustable
1.2 sun (High Intensity)
Device tolerance testing
1.0 sun (STC)
Standard efficiency calibration
0.3 sun (Low Light)
Indoor/low-light performance evaluation
Transient Pulse Mode
Pulse > 200ms
Suitable for rapid I-V characteristic measurements, effectively avoiding the impact of device overheating on test results.
Steady-State Continuous Mode
24h - 1000h
Specifically designed for long-term stability testing and aging experiments, meeting perovskite device lifetime evaluation requirements.
10,000+ Hours
LED Light Source Lifetime
Water Cooling
Standard Industrial System

## Slide 6
Complete Solution Comprehensive Support from Equipment to Service
Turnkey System Configuration
Main System
LC-LED-AAA-300S Solar Simulator Host
Power System
Standard 5000W isolation transformer, ensuring power stability
Cooling System
Standard industrial-grade water chiller, ensuring stable long-term operation
Optical System
Built-in optical integrator and multiple lens groups, collimation angle < 5°
Professional Service Guarantee
Installation & Training
Free on-site installation, commissioning, and operation training
Technical Support
Instant phone support on working days, answering technical questions anytime
Rapid Response
48-hour on-site service commitment, reducing downtime
Quality Assurance
One-year free warranty for the entire machine, long-term supply guarantee for core components
Application Environment Recommendations: To ensure optimal performance, it is recommended to use in a constant temperature and humidity environment with air conditioning, with ambient temperature preferably not exceeding 25℃.

## Slide 7
Why Choose Lecheng Intelligent?
Technology Leadership
International A+ standard certification Optical shaping system ensures testing accuracy
Professional Focus
Designed specifically for perovskite PV applications Precise spectral matching across all bands
Flexible & Reliable
Dual-mode operation, wide-range adjustment 10,000-hour ultra-long lifetime
Comprehensive Service
From installation training to after-sales maintenance Full-range professional support
Lecheng Intelligent
Let us work together to drive innovation and development in perovskite photovoltaic technology

## Slide 8
Looking forward to creating the future with you
Get in Touch
Tel
+86-153-2185-6437
Email
wj.yan@lcintel.com
Address
苏州市常熟经开区科创园5号楼
钙钛矿检测领域最专业、最高效的智能化解决方案。
Lecheng Intelligence Technology (Suzhou) Co., Ltd.
Lecheng Intelligence Technology (Suzhou) Co., Ltd.